Bringing up the Tangerine SDR
Getting Started with
Tangerine-SDR on the
MAX10 Dev Kit using the
Tangerine Data Engine Adapter.
These instructions ARE NOT for use with the final Tangerine Data Engine.

---
Prerequisites
Intel MAX10 Development Kit DEV-10M50-A (with HMAC connector, 2 x GBE connectors).
Includes Wall-wart Power Supply and USB JTAG programming cable
Computer running Centos7 (recommended). Fairly powerful processor with 8G - 16G RAM.
Runs Intel (Altera) Quartus and NIOS (Eclipse) software
Also recommend VSCode to run the Python-based CLI (Command Line Interface).
Ubuntu 20.04 has been used but has some issues.
USB Port and DEV-Kit supplied cable to connect this computer to the DEV-KIT.
Gigabit Ethernet Switch providing DHCP addresses to clients.
Plus Ethernet cable to connect to the DEV-KIT
Computer running Windows 10 with USB port (one-time usage)
UBLOX ucenter software, USB to micro USB cable.
Tangerine SDR Data Engine Adapter
Tangerine SDR Clock Module (Rev A with two reworks).
GPS Antenna plus adapter to SMA.
Tangerine SDR Receiver Module.

---
Preliminary Steps
Test the Dev-Kit prior to Tangerine SDR use.
  1. Connect Dev-Kit via Gigabit Ethernet to switch using bottom GbE connector.
  2. Power up the Dev Kit with it’s included power supply.
  3. Use web browser to verify connectivity to the default Dev-Kit pre-loaded software image.
  4. Write down and safely store the MAC address and Serial Number of your Dev-Kit board.

---
T-SDR Software
- The TSDR software is located at:
  - https://github.com/Tom-McDermott
    - TSDR-Dev is the package that runs on the Dev kit
      - Contains the Verilog and C-code, configuration files, etc.
    - TSDR-Util is a Python command line CLI to
      - Discover the dev-kit using OpenHPSDR.
      - Open a provisioning channel.
      - Provide commands to read and write the module control registers using LH-DE protocol (via UDP sockets).
      - Print Ak / Nak / Text responses to commands.

---
T-SDR Steps (1)
1. Install free version of Quartus Version 20.1 from Intel website onto Centos7.
2. Install free version of ucenter from ublox onto the Windows 10 computer.
3. Make 2 reworks to the Clock Module Version A.
4. Install clock and receiver modules on the Data Engine Adapter (DEA).
5. Install DEA onto the Dev-Kit HMAC connector using stand-offs.

---
T-SDR Steps (2)
1. Configure switches on the DEV-KIT.
2. Install git on Centos 7 if not already there.
3. Install Python 3 on Centos 7 if not already there.
4. Git clone TSDR-Dev and TSDR-Util from github into their respective directories on Centos 7.
5. Power up the Dev Kit.
6. Configure the Clock Module GPS ZED-F9T using the USB-to-Micro USB cable and ucenter software.
  1. Flash the changes to the GPS unit.
  2. Some USB micro cables are power-only and won’t work.

---
Two Types of Usage
- If you just want to run the existing code then no editing or re-compilation is needed.
    - Download the already-built SOF file to the Dev-Kit and starting the FPGA.
    - Download the already built C-code image to the FPGA.
- If you want to modify the Verilog and/or C Code, more extensive work is needed, including:
    - Editing the Board Support Package file (to change some absolute file paths to match your system)
    - Re-synthesizing the Verilog Platform Designer (Q-sys) package.
    - Re-compiling the Verilog.
    - Re-building the Board Support Package (configures the C driver package).
    - Re-patching the Ethernet driver C-code.
    - Re-compiling the C-code.